LTSP – Hardvare

# Scanners
This information is for LTSP 4.2+ and does not apply to previous versions.
## Enable saned on terminal
1. Edit /opt/ltsp-4.2/i386/etc/lts.conf and add XINETD_SERVICES = "saned" to the [default] or relevant terminal section
2. Restart the terminal
3. Run scanimage -L on workstation shell to verify that scanner has been detected
## Usage
1. Edit /etc/sane.d/net.conf and add the hostname or address of client running saned
2. xsane, OpenOffice.org, GIMP, and other scanner-aware applications should now list the scanner
## Troubleshooting
Try this in a terminal window to set the sane network backend to use the current workstation:
SANE_NET_HOSTS=`echo $DISPLAY | cut -d: -f1`
export SANE_NET_HOSTS
-- TimothyLegge - 11 Jul 2006
For more information on this subject see: http://marc.theaimsgroup.com/?l=ltsp-discuss&m=114605694207297&w=2

# Sound cards hardware and drivers
This page is about hardware and drivers. For software, see Sound.
## On-board Sound Cards may be ISA
It is important to note that some on-board sound cards are actually ISA devices. If enabling the sound as above results in errors when booting the client then you may have an ISA sound card. You can gain some clues by looking in the bios; if the sound card is in "other devices" or not listed with the PCI devices it is probably ISA. In this case you will need to supply the following addition to the sound options above:
[ws001]
   SOUND = Y
   SOUND_DAEMON = nasd #or esd
   SMODULE_01 = "sb io=0x220 irq=5 dma=1"
Obviously the correct driver, io address, irq and dma must be provided.
-- JimMcQuillan - 05 Dec 2004
-- RichardJune - 13 Dec 2004
-- TimothyLegge - 15 Apr 2005
The io address must be hexadecimal io=0x220.
-- MarkusG - 13 Oct 2005
## AC'97 Sounds
If you have AC'97 sound onboard,Maybe you hear from microphone line.Not speaker line. --Main.MohsenPahlevanzadeh 18 May 2005
## SiS 7019
SiS 7019 driver for 2.6 kernel
SiS 7019 driver for 2.4 kernel
If you want to use the SiS? 7019 driver for kernel version after ~2.6.8, you'll need to edit the file sis7019.c. At lines 1639 and 1640, remove the following two lines:
   if (remap_page_range(vma, vma->vm_start, virt_to_phys(dmabuf->rawbuf),
        size, vma->vm_page_prot))
and substitute the following three lines:
        if (remap_pfn_range(vma, vma->vm_start,
        virt_to_phys(dmabuf->rawbuf) >> PAGE_SHIFT,
        size, vma->vm_page_prot))
See William Lee Irwin III's patch for the SiS7018/Trident OSS driver
## Improper detection
Sometimes LTSP will misdetect the soundcard. I have a workstation where it actually has Ensoniq ES1371 chip, but LTSP loaded i810_sound module instead.
Assuming your soundcard is PCI (not ISA), here's the way to find out the real sound chip in your workstation: cat /proc/pci
If you see more than one "audio controller", then you'll need to experiment to see which one is the right one.
You can force LTSP to load different sound module than the one it detected by putting the following line into lts.conf: SMODULE_01 = "es1371"
The line above will force LTSP to load es1371 module (instead of whatever it detected)
-- HarrySufehmi - 12 Sep 2005
## Sound on Imac Indigo as a thin client
I have sound working fine on Imac Indigos( shiney cased Macs) now. I tested with xmms, flash enabled sites, and tuxtype2. If,when booting up ,after the usb lines you will get your mac soundcard detection ,same as PC bootup. If you see Powermac Screamer detected as your soundcard the following config in /added to /opt/ltsp/ppc/etc/ lts.conf will make this soundcard work. It appears that on the Bondis( dull colored Macs) the soundcard is initialized correctly,,but there is no sound output?.K12LTSP/FC3 detects the card as a Powemac Burgandy. this card will NOT work.
SOUND = Y SOUND_DAEMON = "esd" VOLUME = 99 X4_MODULE_01 = glx SMODULE_01 = "soundcore.o" SMODULE_02 = "dmasound_pmac.o" SMODULE_03 = "dmasound_core.o"
-- BarryCisna - 05 Mar 2006
## using esd + ALSA drivers in LTSP 4.2
See: http://wiki.ltsp.org/twiki/bin/view/Ltsp/WorkInProgress#esd_ALSA_sound_on_LTSP_4_2
to top

End of topic
Skip to action links | Back to top

I	Attachment	Action	Size	Date	Who	Comment
	SiS7019_driver_source_2.6.zip	manage	20.4 K	11 Oct 2005 - 16:53	JimMcQuillan	SiS? 7019 driver for 2.6 kernel
	sis7019_IA_release_2003_02_18.tgz	manage	25.1 K	11 Oct 2005 - 16:53	JimMcQuillan	SiS? 7019 driver for 2.4 kernel

# Network Cards
The Network interface card is what connects your computer to the local network. The Network interface card is often known as the NIC.
LTSP works fine with 10mbit, 100mbit and 1000mbit (Gigabit) cards. It works with both ISA and PCI cards, although it's a bit easier with the PCI cards, because they can be autodetected. The ISA cards require a couple extra parameters in dhcpd.conf.

## Configuring network booting
In order to boot an LTSP client, the terminal will initialize the NIC twice. The first time, the terminal needs to use the NIC to download a kernel. This first initialization can be done a couple of ways, outlined below:
1. Bootrom Option
2. PXE on card
3. Boot floppy or CD
  1. Rom-O-Matic
### PCI Network Interface Cards
PCI cards should work without special options
### ISA Network Interface Cards
ISA NICs usually are not equipped with a PXE ROM, so you are most likely to use them with Etherboot. Etherboot requires the NIC to be in "jumpered" (fixed address by setting switches or jumpers on the board) or "jumperless" (fixed address by software like RSET8029) mode, while Plug and Pray in most cases will not work. So please make sure to setup the card appropriately. Etherboot will then autodetect the required settings, but the Linux kernel will not, as auto-probing for ISA devices is not done. Instead, you need to hand the kernel a hint which NIC driver to load, and as the NIC needs to be initialised before any access to the lts.conf file is possible, this hint needs to be passed on the kernel command line.
Assuming you are using the ISC DHCP daemon Version 3, you should add those lines at the beginning of your dhcpd.conf:
option option-128 code 128 = string;
option option-129 code 129 = text
so that these two additional options are accepted by the DHCP daemon. If you leave those out, DHCP probably will refuse to start. Any configuration examples on the web that use option-128, but do not specify those option definitions probably apply to DHCP Version 2 (outdated for several years now) which recognized option-128 by default. It had other shortcomings and lack of flexibility, so going with V3 usually is a good idea.
In the host { hardware ethernet ... } section of the client it applies to, insert those two lines:
option option-128 e4:45:74:68:00:00;
option option-129 "NIC=ne IO=0x300";

where the option-128 is a "magic number" telling etherboot that this options are valid and should be respected. For clearing things up, it's not a MAC address, but rather a string äEth followed by the option parsing version number (happing to be 0.0 right now).
In option-129, you can give the NIC module name (ne is rather popular, meaning it is a so-called NE2000 compatible card; 3c509 is another popular one). Additionally you can give the NIC's io address (ioport) and the IRQ (interrupt line); which one is really needed depends on the NIC module to use. Giving the IO at least should be on the safe side, as it avoides any autoprobing.
Options allowed for Etherboot can be looked up in the Etherboot User Manual, at http://www.etherboot.org/doc/html/userman/a838.html
##### 3Com 3c509
The 3Com 3c509 is a very popular ISA based network card. It works well with LTSP, but it needs to be configured properly. The following needs to be done, for the 3c509 to work:
1. You need to DISABLE the plug-n-play on the card. To do this, you'll need the 3com utility http://www.3com.com/products/en_US/result.jsp?selected=5&sort=effdt&sku=3C509&order=desc.
2. You'll need to add
        option option-128 e4:45:74:68:00:00;
        option option-129 "NIC=3c509";
to the dhcpd.conf file. More about option-128 can be found here http://www.etherboot.org/doc/html/userman/a838.html. Please be sure to read it.

## After configuring network booting
Once the terminal is able to start executing a kernel, the kernel itself will need to know what driver to load. If this cannot be autodetected, then the correct module will have to be listed in the lts.conf file.
### PCI Network Interface Cards
PCI cards should be auto-detected by the LTSP kernel
### ISA Network Interface Cards
You may have to specify which module to load via the dhcpd.conf file, see above.
-- JimMcQuillan - 07 Dec 2004
-- SteveSwitzer - 08 Dec 2004
-- AnselmMartinHoffmeister - 05 Jan 2005 (Adding option-128/129 information)

# Video cards
## Specific card settings
### Nvidia
#### nVidia for LTSP-4.1.1
Here's a method for adding the proprietary nvidia modules to the LTSP-4.1.1 system: NvidiaLtsp411
# nVidia proprietary drivers for LTSP-4.1.1
This only works with 4.1.1 as far as I know. It contains the nessecary files for the 2.4 kernel and 2.6 kernel
Review the NVIDIA Software License
You will need to accept this license prior to downloading any files.
Download the driver package from here. This is version 1.0-7174 of the driver.
Copy the file to the client root directory of the LTSP server (probably /opt/ltsp/i386) and unpack it with
tar xvfz nvidia-driver-bin.tar.gz
The files will be placed in the right folders.
Now you just configure your NVidia-clients in lts.conf like this to get hardware accelerated graphics:
[ws002]
  XSERVER = nvidia
  MODULE_01 = nvidia
  X4_MODULE_01 = glx

To create the drivers yourself you may follow these instructions.
Download NVidia drivers from nvidia.com and extract the driver by running the installer with the -x extenstion.
wget http://download.nvidia.com/XFree86/Linux-x86/1.0-8178/NVIDIA-Linux-x86-1.0-8178-pkg1.run
 sh ./NVIDIA-Linux-x86-1.0-8178-pkg1.run -x

Rename the extracted catalog to "nvidia-driver" and make a tar.gz of it, and put the resulting file into the tarballs directory in the LBE (I assume LBE is located in /usr/local/lbe):
 mv NVIDIA-Linux-x86-1.0-8178-pkg1 nvidia-driver
 tar cvfz nvidia-driver.tar.gz nvidia-driver/
 mv nvidia-driver.tar.gz /usr/local/lbe/tarballs/

Change into directory /usr/local/lbe, and make an nvidia-driver folder:
 cd /usr/local/lbe
 mkdir kernel-src/nvidia-driver/

Make a package.def file in this folder, and fill it with the following content:
VERSION = 1.0
RELEASE = 8178

PKG1 = nvidia-driver.tar.gz

MD5SUM1 = 0874c6700f9995f2d1db2bce03240bc8

SOURCE1 = http://download.nvidia.com/XFree86/Linux-x86/1.0-8178/NVIDIA-Linux-x86-1.0-8178-pkg1.run

UNPACK1 = gunzip < ${TARBALL} | tar xf -

BUILDDIR = nvidia-driver

INSTALL = export PATH=/ltsp-src/util-linux/util-linux-2.11z/sys-utils/:$PATH && ./nvidia-installer --kernel-source-path=/kernel-src/linux-2.6.9/linux-2.6.9 --no-runlevel-check --no-rpms --expert --no-network --kernel-name=2.6.9-ltsp-3

CLEAN = rm -rf ${BUILDDIR}
Now make a link in the build environment to bypass some problems with kernel module placement.
chroot /usr/local/lbe
ln -s /opt/ltsp/i386/lib/modules/ /lib/
exit
Start building the driver by doing:
cd kernel-src
./build --only=nvidia-driver
The install program for the NVidia driver is started. Accept the license.
- Confirm Kernel module installation path: "/lib/modules/2.6.9-ltsp-3/kernel/drivers/video".
- Confirm Kernel source path: "/kernel-src/linux-2.6.9/linux-2.6.9".
- Confirm X installation prefix: "/usr/X11R6"
- Confirm OpenGL? installation prefix: "/usr"
- Confirm Installer installation prefix: "/usr"
- Answer no to "Install NVIDIA's OpenGL? header files?". Those won't be needed.
- Answer "Yes" when asked to confirm installation steps and then "OK" when "Installation complete" message is displayed.
The drivers are now loaded into the lbe, but some files are misplaced, so we need to move those files: Change to lbe root directory:
cd ..
and start moving files:
mv -f usr/lib/libGL.so* opt/ltsp/i386/usr/lib/
mv -f usr/lib/libGL.la opt/ltsp/i386/usr/lib/
mv -f usr/lib/libGLcore.so.1* opt/ltsp/i386/usr/lib/
mv -f usr/lib/libnvidia-tls.so.1* opt/ltsp/i386/usr/lib/

We can now make a packed driver file to install into our LTSP 4.1.1 environment:
cd opt/ltsp/i386
tar cvfz nvidia-driver-bin.tar.gz usr/lib/libGL.so* usr/lib/libGL.la usr/lib/libGLcore.so.1* usr/lib/libnvidia-tls.so.1* usr/X11R6/lib/modules/extensions/libglx.so* usr/X11R6/lib/modules/drivers/nvidia_drv.* usr/X11R6/lib/libXvMCNVIDIA* lib/modules/2.6.9-ltsp-3/kernel/drivers/video/nvidia.ko lib/modules/2.6.9-ltsp-3/modules.dep

Install the driver into your operational LTSP environment by copying the driver file into the client root directory of your LTSP server installation and unpack the file. E.g:

cp nvidia-driver-bin.tar.gz /opt/ltsp/i386
cd /opt/ltsp/i386
tar xvfz nvidia-driver-bin.tar.gz

Now you can use the NVidia driver by setting up the client in lts.conf something like this:

--/opt/ltsp/i386/etc/lts.conf-----------------------------
[ws002]
  XSERVER = nvidia
  X4_MODULE_01 = glx
  MODULE_01 = nvidia

#### nVidia for LTSP-4.2 update-2
Peter Ehrenberg has created a page and packages for using the nVidia binary module with LTSP-4.2 update-2.
### sis cards
The SiS driver requires the glx module to be loaded. If you have workstation ws002 that has a sis card, then you would specify this:
[ws002]
  X4_MODULE_01 = glx
### S3 and S3Virge cards
The support for S3 and S3Virge cards may still be a problem in XFree86 4.x and X.org, so LTSP provides the older XFree86 3.3.6 versions of the drivers, which work quite well on those older cards. Try the Xorg s3virge driver first.
If you have a workstation that has an S3 or S3Virge card, you would specify the older driver like this:

[ws003]
  XSERVER = XF86_S3 (or XF86_S3V for the S3Virge card)
If the driver name starts with XF86_, that means it will use the older 3.3.6 version of XFree86.
If you have an S3 Trio video card, these settings work well:

[ws003]
  XSERVER = XF86_S3
  X_VIDEORAM = 4096
  X_COLOR_DEPTH = 8
  X_MODE_0 = 800x600 40 800 840 968 1056 600 601 605 628 +hsync +vsync

That will set video RAM to 4mb, color depth to 256 colors, and display mode to 800x600. Higher color depths were causing the screen to flicker, but this one sacrifices a few nice colors for that.
### Via embedded graphics
Via Unichrome graphics as included in their mini-itx systems seem to have problems with autoconfiguration. They do not autodetect and the via driver must be explicitly specified. They will work without specifying the driver, but will use the much slower vesa driver.
If you have a workstation based around a Via mini-itx motherboard, you would specify the via driver like this:

[ws003]
  XSERVER = via

You may need to specify the monitor's refresh rates explicitly as well, as described in the next section of this page.
While starting X with the via driver, you may see errors indicating that certain symbols are not defined. These can be ignored and will not effect functionality.
#### Via embedded DVI Interface
Starting with Xorg 6.9.x, detecting a DVI interface is unreliable for the LTSP Term 170. The following lts.conf option forces X to use the DVI interface:

[ws003]
  X_DEVICE_OPTION_02 = "ForcePanel true"

This applies to LTSP versions >= 4.2
If you are running LTSP installed from Ubuntu or Debian packages beginning with Ubuntu Edgy or Debian Etch, create a custom xorg.conf for a DVI workstation adding the following to lts.conf:

[ws003]
  XF86CONFIG_FILE = /etc/X11/xorg.conf.ws003

xorg.conf.ws003 Monitor section is where you add the ForcePanel? option:

Section "Monitor"
        Identifier "Generic Monitor"
        Option "DPMS"
        HorizSync 40-75 # Set this to match your monitor's specs
        VertRefresh 50-85 # Set this to match your monitor's specs
        Option "PanelSize" "1280x1024" # Useful if your monitor's maximum
        # resolution is greater than the X video
        # resolution you are running
        Option "ForcePanel" "true" # Forces use of DVI interface
EndSection
### Geode GX1
Ok guys, I finally sat down this weekend, and decided to see what I could do about the Xserver for the Geode GX1 chipset in the Jammin-125.
I found the old driver that Alan Hourihane wrote back in 2002, and I compared it, almost line for line with the latest driver in Xorg 6.8.2.
The old driver was called "geode", but they changed the name when they added support for the GX2 chipset. The driver is now called "nsc" which stands for "National Semi-Conductor".
In the latest driver, all of the code to handle the GX2 is implemented in a separate file, so there's a clear distinction between the GX1 code and the GX2 code.
Anyway, I compared line for line, the GX1 driver code, and I found no significant differences. There's some new options, to enable/disable certain features, but nothing that should affect the stability of the driver.
So, I started testing the nsc driver. I used x11perf, and I found that the driver kept failing. After several tests, I found that it was failing in the same place, running the same test. I saw in the /var/log/daemon file that GDM was having a problem contacting the Xserver. The actual message was:

 localhost gdm[4960]: Ping to ws251.ltsp:0 failed, whacking display!

I thought it was because the Xserver was crashing, and GDM could no longer Ping the Xserver, so it reported the error.
Turns out that's not the case.
There's an operation in x11perf that takes 72 seconds to complete on the GX1 chipset. GDM sends a ping (not an icmp ping, it's actually a GetFontMetrics? request). If GDM doesn't get a response within 15 seconds, it assumes the Xserver has dissappeared, so it stops managing the session. Gives the screen the appearance that the Xserver has locked up.
SO, if I run the Xserver standalone, without querying the display manager, and then I run x11perf from my desktop with a '-display ws251:0.0', it will run x11perf, displaying on the GX1 chipset, it runs the entire test to completion. No crashing, no hanging.
I ran the test several more times, and on the 3rd attempt, the computer locked up. I'm thinking this is heat related, because it's hot in my office, and i've really been punishing this GX1 chipset. I tried rebooting the client, and I couldn't get X to run on it. I turned it off, and left it for about 2 hours, and then when I went back to test it, it performed fine again. Like I said, looks like a thermal problem, but i'm not too worried about it. In a normal office setting, nobody is going to push the chipset as hard as I did.
I need to modify the vidlist file to cause the 'nsc' driver to be loaded, instead of the non-existant 'geode' driver. That'll be out in the next update of LTSP. Until then, people just need to add the following line to their lts.conf file:

   XSERVER = nsc

OR, they could modify the vidlist file and change:

  1078:0104 geode
to read:
  1078:0104 nsc
Then, autodetection will cause the proper driver to be loaded.
-- JimMcQuillan - 26 Jun 2005
## Xinerama / TwinView?
LTSP 4.2 introduces multiple monitor support, example configuration discussed in the mailing list archive:
http://www.mail-archive.com/ltsp-discuss@lists.sourceforge.net/msg26519.html
With multiple monitors, keyboards, mice, and sound devices it is possible to setup a Multi-Seat environment in which multiple users can share one terminal.
## Setting resolution
LTSP uses a default resolution of 1024 x 768. You can override this by adding entries to your /opt/ltsp/i386/etc/lts.conf file.
You can specify either a full modeline (like the example for ws008) or a simply resolution. A useful tool to generate these modelines can be found at http://koala.ilog.fr/cgi-bin/nph-colas-modelines.
Another useful tool to generate a modeline can be found at http://xtiming.sourceforge.net/cgi-bin/xtiming.pl

  [ws001]
    X_MODE_0 = 800x600

  [ws008]
    #
    # ATI Card with ViewSonic P815 21" monitor running at 1800x1440
    #
    X_MODE_0 = 1800x1440 250 1800 1896 2088 2392 1440 1441 1444 1490 +HSync +VSync
    X_HORZSYNC = 30-115
    X_VERTREFRESH = 50-160

  [ws009]
    #
    # 17" flat panel. Had to add the X_HORZSYNC, otherwise it would do only 1280x960
    #
    X_MODE_0 = 1280x1024
    X_HORZSYNC = "60-70"

You can specify up to 3 resolutions, using X_MODE_0, X_MODE_1, and X_MODE_2. Then, you can cycle between the resolutions, using the Ctrl-Alt-KP+ key. For example:

  [ws001]
    X_MODE_0 = 800x600
    X_MODE_1 = 640x480
    X_MODE_2 = 1024x768
## Video drivers
Most PCI video cards work very well with LTSP. Some, however, are a bit of a problem.
The PCI video cards can be autodetected during the boot process, so there is usually nothing that needs to be set. Sometimes, you may want to force a certain Xserver to be used. You do this with the XSERVER parameter in the lts.conf file.
For instance:

  [ws001]
    XSERVER = ati

The above example will for the ati module to be loaded by the Xserver. Figuring out which Xserver module to load depends on whether you want to use the X.org Foundations Xserver, or the older XFree86 3.3.6 Xserver.
### X.org
The X.org Xserver is a modular Xserver that has a generic core, and many loadable modules. The current list of X.org driver modules:
- apm
- ark
- ati
- atimisc
- chips
- cirrus
- cyrix
- dummy
- fbdev
- geode
- glint
- i128
- i740
- i810
- mga
- neomagic
- nsc
- nv
- r128
- radeon
- rendition
- s3
- s3virge
- savage
- siliconmotion
- sis
- tdfx
- tga
- trident
- tseng
- vesa
- vga
- via
- vmware
### XFree86 3.3.6
If you specify a value for the XSERVER parameter that starts with XF86_, that will cause the terminal to use a 3.3.6 XFree86 Xserver. The 3.3.6 Xservers are in the /opt/ltsp/i386/usr/X11R6/bin.
The XFree86 Xserver is many completely separate Xserver binaries.
The current list of XFree86 3.3.6 Xservers:
- XF86_3DLabs
- XF86_8514
- XF86_AGX
- XF86_I128
- XF86_Mach32
- XF86_Mach64
- XF86_Mach8
- XF86_Mono
- XF86_P9000
- XF86_S3
- XF86_S3V
- XF86_SVGA
- XF86_VGA16
- XF86_W32
## How much video memory do I need?
(or - what is the maximum resolution I can get on my xMb card?)
To calculate the video memory required you have to multiply the horizontal resolution, vertical resolution and colour depth and divide it by 8.

memory required (in bytes) = horisontal resolution * vertical resolution * depth (in bits) / 8
for example:

1024 * 768 * 24 / 8 = 2,359,296
1024 * 768 * 16 / 8 = 1,572,864

thanks to Kalev Lember
nvidia-driver-bin.tar.gz: Nivida Drivers for ltsp 4.1 with kernels 2.4 and 2.6
## X Servers
LTSP 4.1 ships with XFree 3.3.6 and X.org ?? * LTSP 4.2 ships with X.org 6.9

# Input Devices
This page is for covering alternate input devices, like touch screens and tablets.
-- JimMcQuillan - 08 Mar 2005
## Wacom Tablets
Wacom support is included as a module in the LTSP kernel. Here is how to get a USB Wacom tablet working with LTSP's 2.6.9 kernel and Xorg. In order to activate it you need to modify your lts.conf file, normally located at /opt/ltsp[version]/i386/etc/lts.conf. Add the following lines:

        HOTPLUG = Y
        MODULE_01 = uhci-hcd
        MODULE_02 = usbhid
        MODULE_03 = wacom
        X_MOUSE_PROTOCOL = "imps/2"
        X_MOUSE_DEVICE = "/dev/input/mouse0"
        X4_MODULE_01 = wacom
Of course you might have other modules in your lts.conf file so adjust accordingly. My file includes lines for a USB mouse, note that if you intend to use a USB Wacom tablet with a USB mouse don't set the mouse for /dev/input/mice or it will conflict with the Wacom mouse.
Next, /opt/ltsp/i386/etc/build_x4_cfg needs some modifications. Add the wacom specific input devices in the server layout:Section

"ServerLayout"
        Identifier "XFree86 Configured"
        Screen 0 "Screen0" 0 0
        InputDevice "Keyboard0" "CoreKeyboard"
        InputDevice "Mouse0" "CorePointer"
        InputDevice "Mouse1" "AlwaysCore"
        InputDevice "cursor" "SendCoreEvents"
        InputDevice "stylus" "SendCoreEvents"
        InputDevice "eraser" "SendCoreEvents"

Modify the mouse input device section:

Section "InputDevice"
       Identifier "Mouse1"
       Driver "mouse"
       Option "Device" "${X_USBMOUSE_DEVICE:-"/dev/input/mouse0"}"
       Option "Protocol" "${X_USBMOUSE_PROTOCOL:-"PS/2"}"
       Option "BaudRate" "${X_USBMOUSE_BAUD}"
       Option "Resolution" "${X_USBMOUSE_RESOLUTION}"
       Option "Emulate3Buttons" "${USBEMULATE_3_BUTTONS:-"off"}"
       Option "ZAxisMapping" "4 5"
       Option "Buttons" "${X_USBMOUSE_BUTTONS:-"3"}"
EndSection

Again, make sure to change from "/dev/input/mice" to "/dev/input/mouse0" for the same reasons as stated above. Finally--Add the wacom input devices to build_x4_cfg right after Mouse1:

Section "InputDevice"
        Driver "wacom"
        Identifier "cursor"
        Option "Device" "/dev/input/event2"
        Option "Type" "cursor"
        Option "Mode" "relative"
        Option "Suppress" "2"
        Option "USB" "on"
        Option "ZAxisMapping" "5 4"
EndSection

Section "InputDevice"
        Driver "wacom"
        Identifier "stylus"
        Option "Device" "/dev/input/event2"
        Option "Type" "stylus"
        Option "Mode" "absolute"
        Option "USB" "on"
        Option "Tilt" "on"
        Option "Threshold" "20"
        Option "HistorySize" "200"
EndSection

Section "InputDevice"
        Driver "wacom"
        Identifier "eraser"
        Option "Device" "/dev/input/event2"
        Option "Type" "eraser"
        Option "Mode" "absolute"
        Option "USB" "on"
        Option "Tilt" "on"
        Option "Threshold" "20"
        Option "HistorySize" "200"
EndSection

Note that my configuration uses /dev/input/event2 for the Wacom tablet. That may not be the case on your system. To find out, open a console on the client and cat /dev/input/event[x] and draw on the tablet to see if that's where it is seeing the tablet.
Hint: put this in your lts.conf and you can switch to a console with a Control + Alt + F2.

 SCREEN_01 = startx
 SCREEN_02 = shell

I've got a client that will switch from event2 to event1 or event0 depending if the system was booted up with the tablet plugged in or plugged in after boot up and which USB port is used.
This worked great until I got a brand new Wacom Intuos3 tablet. Intuos3 support wasn't added to the kernel until 2.6.12. I was able to build a 2.6.12 kernel in LBE, but it doesn't have supermount and may be pushing the envelope a bit too far. However, it was rather easy to get some new components from the the linux-wacom project, http://linuxwacom.sourceforge.net/ and make a patch that works for the LTSP 2.6.9 kernel. You can do it yourself in LBE or if you just want to get your tablet working simply get the Wacom-kit I included here and copy the modules in there proper location.
There is still some more work to be done. I'd like the X configuration to skip the Wacom sections is there is no tablet attached and to make a wacom link in /dev/input. This will be much easier once LTSP switches over from devfs to udev.
One more thing--Intuos3 has a "pad" feature that can be added to the X configuration but I haven't figured that one out yet.
Clearly this tip can use some improvement so please, feel free to edit this.
-- DanielFort - 29 Aug 2005
If you want to try building a 2.6.12 kernel in LBE, posted is the kernel-src that worked for me. Note that I took out the 2.4 kernel and supermount but I did apply the 2.6.12.5 kernel patch. Simply replace the kernel-src directory with this one and it should work.
-- DanielFort - 22 Sep 2005
to top

End of topic
Skip to action links | Back to top

I	Attachment	Action	Size	Date	Who	Comment
	wacom-kit-2.6.9.tar.bz2	manage	12.3 K	29 Aug 2005 - 04:57	DanielFort	Pre-built Kernel Modules
	wacom-lbe-kit-2.6.9.tar.bz2	manage	7.1 K	29 Aug 2005 - 04:58	DanielFort	Wacom patch for LBE
	linux-2.6.12_kernel-src.tar.bz2	manage	78.0 K	22 Sep 2005 - 17:56	DanielFort	LBE kernel-src for Linux 2.6.12.5

# Clients
## What's the minimum client
A frequent question I get is: What's the minimum recommended client?.
My basic answer to this question is: Anything with a PCI bus and 32mb of ram.
The PCI bus isn't a strict requirement, but the video chipsets that they put in the ISA bus based machines are really crappy, and usually not worth the fuss.
You can also get by with less than 32mb of ram, but you'll almost certainly want to turn on NFS-SWAP in the lts.conf file. It's probably a good idea to turn on NFS-SWAP even with 32mb. It's a great safety net.
-- JimMcQuillan - 23 Mar 2005
## Another opinion on Minimum clients
LTSP Clients do not require any specific hardware as such but for two requirements. First, the RAM on the Client should be good enough (128MB is a better choice) and the Second is that there should be Network boot facility present in the BIOS of the motherboard and moreover the NETWORK card (along with the BOOTROM) should be supported by the motherboard as i faced some problems when using the network card on the old motherboard. Moreover, we should be very careful if the card is present in the DRIVER database of the OS as many cards are although supported but we need to specify the exact driver which the client requires (in case we are using different cards on different clients).
-- DhirajGaur - 04 Jan 2005
Please add information to this page about specific LTSP client hardware
## Commercial Client LTSP compatibility
Repurposed Commercial Clients Table
## DisklessWorkstations?.Com
### Jammin 125
To use this thin client with LTSP-4.0 and above, you'll need to set the XSERVER to the proper driver.
The entry you'll need in lts.conf is:
XSERVER = nsc
## DisklessThinClients?.com
Great place to comparison shop. All thin clients work with LTSP, and more are added every week. http://www.DisklessThinClients.com Use coupon code: LTSP5P to get 5% off diskless thin clients as an LTSP member.
## TheSymbiont.com
Of particular interest is the SYM1110 (http://www.thesymbiont.com/index.php?option=com_content&task=blogcategory&id=80&Itemid=109)
This one uses the new Geode GX2 chipset. You can ask the Symbio guys for drivers rolled against the 2.4.26-ltsp-3 kernel for OSS audio and the amd Xorg driver for video)
## IBM NetVista clients
### N2800
Just wanted to let everyone know that to get a IBM N2800 is very simple using LTSP, I am running SUSE 9.2 and LTSP, I changed the DHCP to have a host with the correct MAC address, and load PXE. Then I went into the setup utility, although it didn't indicate anywhere it was F1. I changed the authorization setting from RAP to DHCP, and it booted right up.
### N2200
Experiments with netvista Model 8363EXX.This is the work provided by Karl Kappel and augmented by Chris Turner and "John C". Enter the bios using F1 key.You may have to move the jumper on the motherboard if it is password protected..Once in you can hit F5 for advanced configuration options. Go to Configure network settings and make dhcp first network priority..tftp subnet broadcast can remain disabled..
You dhcp server needs to have option 211 enabled. I used these two lines in isc dhcp3 on redhat.
option option-211 code 211=string;
option option-211 74:66:74:70;
At this point tftp transfer should work..By putting blash.2200 in /tftpboot and as filename in dhcpd.conf
you should be able to load the firmware update to most recent (July of 2002).
Add the kernel file provided (vmlinux-2.4.19-LTSP-IBMNC) to /tftpboot/lts and point to it in dhcpd.conf (comment the filename "blash.2200"; When the client boots it should boot to the point where an nfs mount occurs..The IBM firmware does not recognize the root-path directive in dhcpd.conf! Don't forget to restart the services..
The kernel expects to have its root file system where it is booted from.. I futzed with this and think the definitive move was (from /tftpboot) entering ln -s /opt/ltsp/i386 /lts..This allowed nfs mount and brought me up to a shell prompt on the client.
Pehaps the best solution to the root path dilemma is to edit /etc/xinetd.d/tftp and comment the server_args = -s /tftpboot statement..THEN provide the full path to your kernel in filename statement of /etc/dhcpd.conf
Here is a semi-stable link to the tgz provided to me.dont forget the modules folder 2.4.19-LTSP-IBMNC needs to be in /opt/ltsp/i386/lib/modules
http://169.244.61.66/2.4.19-LTSP-IBMNC.tgz
There is an lts.conf provided to start from (in Karl's tgz). I got the best results by commenting the two lines specifying explicit XF86Config files and adding xserver=nsc. Pardon the punctuation and spelling..Just wanted to get this somewhere safe..
Experimental:Using windows dhcp to pass options..Adding option 211 from command line
netsh
dhcp server
add optiondef 211 BOOTPROTOCOL STRING
#########################################
In windows 2000 dhcp

option 12 netvista1 to pass hostname (does not work)
option 17 10.10.10.254:/opt/ltsp/i386
option 66 10.10.10.254
option 67 /opt/ltsp/i386/vmlinux-2.4.19-LTSP-IBMNC
option 211 tftp

Because windows pads the root path with zeros linux client sees the root-path as /opt/ltsp/i386000.The solution is to ln -s /opt/ltsp/i386 /opt/ltsp/i386000
It appears firmware must be at least 12/06/01 to boot linux..but i have reports the firmware upgrade is not necessary
We're working with etherboot to add support for ltsp-4.2 here at Linuxworld Boston
cliebow@ltsp.org
### Model 8362-a53 ppc architecture
Will initiate tftp transfer of yaboot after trying yaboot.63Z yaboot.63a yaboot.Z
Then errs out with Incorrect Product File
Network Station 8362 not supported in file yaboot
### Model 8364
Gary Hurley has written an article for EazyTek. You can view the article here: http://www.eazytek.com/netvista/ltsp.php
## Fujitsu Siemens
### Futro S300
Works just fine with LTSP out-of-a-boz (almost). I just needed to add row for video card in /etc/videolist so LTSP would auto-detect client videocard automatically. Needed row is:
1039:0325 sis

Client normally boots from its internal CompactFlash? card, so it is required to change manually to boot from network from BIOS. But that's all installation that is needed. These clients are also supports XVideo extension so full-screen video is no problem for them.
### Scovery Xs and Futro C
This client works very well with the LTSP. There are no main issues in booting the client, except for choosing the PXE lan boot, and getting rid of the 32MB flash memory that usually comes incorporated.This client comes with no floppy or hard disk, but with rs-232, parallel port, audio, vga, and 2 usb ports. I have 25 Scovery Xs and 40 Futro C working everyday.
I have successfully tested:
Power button turns off computer (works well enabling acpid in ltsp 4.1, but requires kernel compilation for version 3). Audio output works well out of the box. Just install ltsp_sound. Local Apps. Tried to run xscreensaver to minimize network traffic, and worked in lab environment reducing dramatically the network traffic. Parallel printer connected and working as print server.
Not tested:
Accessing USB flash memories through server.
-- AntonioMartins? - 16 Nov 2005
## A link to Wyse Winterm Information
http://winterm.gaast.net
## HP t5000 series
### T5125
This client has trouble with Xorg, because the Xorg driver doesn't properly determine the amount of video memory. So, you have to tell it.
Here's the entry you'll need in the lts.conf file:
X_VIDEORAM = 16384

Thanks to Rusek Ondrej and John Ruff for providing this info.
I have this very terminal, rather then specifying X_VIDEORAM, I specified XSERVER=vesa for these units and not only did it properly detect the RAM, but it eliminated a lockup bug, and performed better. -- Richard June
Sound seems to work with these options. -- Asmo Koskinen
SMODULE_01 = soundcore
SMODULE_02 = ac97_codec
SMODULE_03 = via82cxxx_audio
### T5300 and T5500
This client works well with the LTSP. The only known issue is with older BIOS images not being able to PXE boot. The symptom is a failure while downloading either the kernel or initrd image, the download will hang at a random point during one of the transfers. The problem appears to have been fixed in version 1.07 and above.
Its possible to have the system PXE boot without adjusting the boot order by pressing F12 while the system is coming up.
## The ThinCast 5000 or ThinClient 5000
Clinet works suitably with LTSP. Supports PXE boot and both sound and limited video. Has AMD Geode architecture. Probably the exact same model as some other thinclients as it was made by ImageBank. I had it playing video and music with XINE but then response for everything else went downhill. Works fine for browsing and abiword.
* Press F1 after power-on to PXE boot. * Server type should be nsc but also works as VESA * Sound can be enabled using:
Needed Assistance
Getting into boot ROM
## eBox
### eBox-II / eBox-150LS
The eBox-II is probably the cheapest thin client around that works great with LTSP.
Specs:
- Vortex86 200MHz processor with Fan
- Realtek 8100B 10/100M
- 128 MB RAM
- 32MB Shared Video Mem so accelerated drivers can be used (With new BIOS)
- PXE Boot
Sound drivers can be a bit problematic to install but this should be fixed in the latest version of LTSP
In Cape Town we have about 100 units running 24/7 for more than a year now and we have had no fan or heating failures. Running these is cheaper than running refurb PCs.
http://www.msti.com.tw/
-- MarcelBerteler - 31 Aug 2006
## DELL
### GX280 (with optional RADEON X300 video card)
This client works well with the LTSP. The only issue is related to the eth card possibly not recognised by LTS boot kernel. The solution is to add NIC=tg3 to the kernel parameters in /tftpboot/lts/2.6.9-ltsp-3/pxelinux.cfg/default
A working dual head XF86Config file is available on www.SuperAlberT.it
-- AlberT - 13 Sep 2005
### Optiplex SX270
The Optiplex is a small client with some nice features:
- DVI Output
- build-in-graphics (resolution 1280 x 1024)
- silent (but not noiseless) fan
- good relation of price and performance
- build-in dvd-rom (optional)
- boot via pxe
This client could be provided with different Intel CPU's (Pentium IV and Celeron), I am using a Celeron M 1.6 GHz with LTSP-4.2. The technical data could be found on the web site of DELL. A hard disk could be installed but of course is not necessary for LTSP.
The configuration is quite simple. In the /etc/dhcp.conf you have to add the following lines (see also the information about booting with PXE:
# fixed address for optiplex sx270
host name_of_your_optiplex {
  hardware ethernet your_mac_address;
  fixed-address your_ip_address;
# root-path and filename must be adapted to your system
  option root-path "192.168.0.8:/opt/ltsp-4.2/i386";
  filename "/lts/2.6.17.8-ltsp-1/pxelinux.0";}
In the lts.conf only some entries are necessary:
 XSERVER = auto
 X_MOUSE_PROTOCOL = auto
 X_MOUSE_DEVICE = "/dev/psaux"

With an older version of LTSP and an older kernel you may not reach the normal resolution.
-- MarkusGoerres - 29 Aug 2006
## Compaq Winterm
This information became a little too big for this page so I have created the CompaqWintermLTSP page.
## Do it yourself thin client
I saw one of the purpose made LTSP workstations from DisklessWorkStations.com at a conference a couple of years ago, and was really impressed. However, the costs of shipping, customs duty, etc made a personal import into Europe prohibitively expensive. On the other hand, it was impossible to buy local alternatives without paying for a copy of Windows CE.
Following a challenge on the LTSP discussion group I decided the only solution was to build my own. I'd never done anything like this before, but it was so easy I thought I'd write up how I did it
-- JPMcC - 23 Mar 2005
## The FAT Client!
FAT? yes, it means your windows, Linux or MACOSX user NEEDS that complete fat computer with operating system installed locally to run that FAT application that has no counterpart in Linux, has not been ported to linux or maybe the dude just insists on keeping the habit.
There are many types of access from a pc with a complete operating system; from GUI to GUI, from Boot to GUI choosing LTSP at boot time and from shell to shell.
### From GUI to GUI:
This gives you both worlds at the same time, your fat pc with ltsp services
#### From GUI to GUI Linux to LTSP server:
Linux of course is native Linux to Linux communication, the sweetest of remote access you can ever have, in here, just run a temrinal and run:
X -query server.name.or.ip :1
But of course, if you want that remote linux GUI in a cute little window, just use Xnest instead of X
Xnest -query server.name.or.ip :1
In both cases ":2" may vary to a higher number depending on the screens you are already working on, your local screen is ":0" and the next one is ":1" so if it's not available, use ":2" and so forth.
#### From GUI to GUI MAC OSX to LTSP server:
IMHO MAC is sweet, it's core kernel is based on UNIX, it runs on X and of course you can just query LTSP!
X -query server.name.or.ip :1
I don't have a MAC so I can't test to see if Xnest is there too
#### From GUI to GUI Windows to LTSP server:
##### X-deeep/32
The most beautyfull results Ive found in Windows is with the FREEWARE X-deeep/32.
http://www.pexus.com/Product_Information/product_information.html
All it does is the regular X -query server, so you do get that feel of locality, of course it's not as fast as the real thing, but will do, once the user sees X at a regular X terminal, he will ask for that too.
##### Xming
Xming is an X Server for Windows based off the X.org source code. You can combine Xming with XLaunch and PuTTY? for one-click launching of remote single applications or whole sessions.
When I want to work in Windows and Linux at the same time, I launch the xfce4-panel as a convenient launcher panel.
-- AndrewZ - 05 May 2006
#### From GUI to GUI Cross-Platform to LTSP server using NoMachine?
NoMachine? optimizes the X protocol to improve performance significantly. From NoMachine?.com: "NoMachine NX is a Terminal Server and Remote Access solution [...]. Thanks to the outstanding compression, session resilience and resource management developed on top of the X-Window system, and the integration with the powerful audio, printing and resource sharing capabilities of the Unix world, NoMachine? NX makes it possible to run any graphical application on any operating system across any network connection as if you were sitting in front of your computer."
Clients are available for Windows, Linux, Mac OS X, Solaris, web browsers, and some handheld devices.
See NoMachine NX and http://freenx.berlios.de/[FreeNX]].
### Boot to GUI choosing LTSP
You either choose ltsp or your fat client
#### Boot to GUI choosing LTSP at Linux boot time
http://rom-o-matic.net/ the same place where you get those eeprom boot images gives you the option to boot from the local hard disk!
Just choose Lilo Bootable ROM (lzlilo) save the file in your /boot directory Add the correct enrty at lilo.conf
image=/boot/thefile.lzrom
label="Linux Terminal"
Save the file and run
# lilo
All as root, once you turn that pc on again, LTSP will be one more option!
#### Boot to GUI choosing LTSP at MACOSX boot time
Hold down the N key when it starts up and it will look for a netboot. Holding down the Option key while booting will present a boot menu which will include any network servers that serve netboot. You can also use the System Preferences to set the default boot source. A PDF with a description of the Macintosh style netbooting is at http://www.dpi-stl.com/whitep/L31751A_NetBoot_TB_final.pdf. Macs support both server and client netbooting and you can adapt Linux clients or servers to work with them.
#### Boot to GUI choosing LTSP at Windows boot time
If your computer is dual booting with Linux, you are already using lilo, so go back 2 steps and do it that way.
What ALSO works, is choosing DOS Executable ROM Image (.COM),
##### For MS-DOS, windows 95, 98, 98SE and related operating systems
get that romomatic ROM image and save it on disk C:\theromimage.COM
Edit C:\CONFIG.SYS and add this to the top:
[Menu]
MenuItem=windows,Microsoft Windows 95/98
MenuItem=linux,Linux (make sure server is running first!)
MenuDefault=windows,10

[linux]
DOS=NOAUTO

[windows]

Edit C:\AUTOEXEC.BAT and add this to the top:
@ECHO OFF
GOTO %CONFIG%

:linux
C:\theromimage.COM

:windows
##### For windows 2000, XP and related operating systems
Open windows' file manager, choose in options to see ALL files right-click boot.ini choose properties UNCHECK "Read Only" checkbox Accept
This will allow you to change the permissions on the boot.ini file. Then, with Notepad, open the boot.ini file.
Hint: You will need to actually type in the filename of the boot.ini file to open it.
Now add the following line below the last line of the file:
C:\theromimage.COM="Linux Terminal"

Save and close the file.
Next, you will need to restore the permissions to the boot.ini file with:
Open windows' file manager, choose in options to see ALL files right-click boot.ini choose properties CHECK "Read Only" checkbox Accept
### From shell to shell:
#### From Linux shell to LTSP shell:
ssh-client comes preinstalled on most linux systems, if you dont have it install with this as root
or compile, google for compile ssh etc
ssh -XC server.name.or.ip
#### From Mac OSX shell to LTSP shell:
open a terminal and run
ssh -XC server.name.or.ip
#### From Windows shell to LTSP shell:
There are many clients for windows, but Id recommend putty download putty
http://www.chiark.greenend.org.uk/~sgtatham/putty/download.html
and connect to the server with it
-- CarlosUrbieta - 30 Apr 2005
## VMWare virtual client
The free-of-charge VMware Player is useful for testing and for accessing the terminal server from Microsoft Windows.
1. Install VMware Player
2. If you use the pre-defined LTSP 4.2 virtual machine image, skip to step 6.
3. Define the virtual machine using EasyVMX!. It seems necessary to set Ethernet in bridged mode.
4. If your terminal server boots from PXE, skip the next step.
5. To boot from Etherboot, use the Etherboot media.
6. Run the .vmx file.
If you want to change the Ethernet MAC, just edit the .vmx file with a text editor.
-- AndrewZ - 05 May 2006
## Qemu as a client
QEMU can be used as an LTSP client on the server. This is very useful for testing. QEMU takes an option of booting an ISO image and emulating an 8390 ethernet device (PCI NE2000). Command line options set the device and MAC address. The client communicates with the host via the TUN/TAP device and uses the bridging function in the kernel.
Getting the ISO image
Download the ns8390.iso from www.rom-o-matic.org. You should be able to use either the NBI or PXE boot images. This example uses eb-5.4.2-ns8390.iso
QEMU
Install the QEMU package for your favorite distribution.
Starting the bridge
The following commands on the host configure the bridge (run as root). The host has to have a valid address on the LTSP client subnet (here it is 192.168.0.101).
brctl addbr br0
brctl addif br0 eth0
brctl stp br0 off
brctl setfd br0 0
brctl sethello br0 1
ifconfig br0 192.168.0.101
ifconfig eth0 down
ifconfig br0 up
ifconfig eth0 up
Configure the QEMU interface script
This script /etc/qemu-ifup on the host adds its interface to the bridge configured above.
#!/bin/sh
/sbin/ifconfig $1
/usr/sbin/brctl addif br0 $1
/sbin/ifconfig $1 up

Configure DHCP
The DHCP server must listen on the bridge. Therefore the DHCP server must start after the bridge has been configured. Add br0 to the DHCP server startup args. Eg: DHCPDARGS="eth0 br0" in /etc/sysconfig/dhcpd and start the server.
Start the client
To start the client run the following command. Note that it needs to run as rootto be able to create a TUN/TAP device.
qemu -cdrom eb-5.4.2-ns8390.iso -boot d -net tap -net nic,macaddr=52:54:00:12:34:56
You should see the client boot in a the terminal window.
-- DarrylBond - 20 Jul 2006
## IGEL
### Igel Winnet 3
A typical terminal client with 32 MB RAM. To work with LTSP booting via PXE is necessary and in the lts.conf you need to choose the following XSERVER:
 XSERVER = nsc
 X_MOUSE_DEVICE = "/dev/psaux"
 X_MODE_0 = 1024x768
-- MarkusGoerres - 01 Sep 2006

# Mice

If you have information about setting up a mouse in LTSP, please edit this page, and add your notes.
## Basics
For basics of setting up a mouse, search for "mouse" in the page lts.conf.
## LTSP 4.1 + USB Microsoft Wireless Optical Mouse 2.0
This may help someone out there...
My system: Compaq EVO510USDT, LTSP 4.1 kernel. XF86Config with the following:

Section "InputDevice"
  Driver "mouse"
  Identifier "Mouse[1]"
  Option "ButtonNumber" "5"
  Option "Device" "/dev/input/mice"
  Option "Name" "Autodetection"
  Option "Protocol" "ImPS/2"
  Option "Vendor" "Sysp"
  Option "ZAxisMapping" "4 5"
EndSection

Results in chaotic mouse behaviour. On inspection, the kernel seems to make a redundant load of the usbmouse module. "rmmod usbmouse" restores sanity.
-- PaulReeve - 20 Dec 2004
## Old hardware can't always autodetect USB mice
Some old hardware doesn't autodetect the presence of a USB mouse. In that case edit /opt/ltsp/i386/etc/lts.conf
and
        X_MOUSE_PROTOCOL = "IMPS/2"

in either the [Default] section (if all your mice are USB or just add it to the specific terminal section if you have a mixed environment
-- PaulZagoridis - 01 Dec 2005
## When all else fails: Older kernel for scrollwheel
I could not get the scrollwheel of my Logi MX1000 to work on a client with kernel 2.6.9. Then I somehow discovered that it works well on another client with kernel 2.4.26. And no, I don't know why.
You may install both kernels in /tftpboot, you just have to set the older kernel in dhcpd.conf for the corresponding client. Then restart the demon (rcdhcpd restart on a SuSE? distribution).
-- AlfredPoschmann - 19 Feb 2006
## Mouse autodetection
See http://wiki.ltsp.org/twiki/bin/view/Ltsp/WorkInProgress#Mouse_Autodetection.