Configure Network Bonding / 2022/06/29

	Configure Network Bonding to bind multiple network interfaces into a single load balanced or fault-toleranced interface and so on. / The Network Teaming feature which is the same solution of network load-balancing or fault-tolerance is also provided. Refer to the comparison of network teaming and bonding features below. / ⇒ https://access.redhat.com/documentation/en-us/red_hat_enterprise_linux/7/html/networking_guide/sec-comparison_of_network_teaming_to_bonding / There are some modes for configuring network bonding like follows. / Mode Mode Name Description / 0 balance-rr Sets a round-robin policy for fault tolerance and load balancing. Transmissions are received and sent out sequentially on each bonded member interface beginning with the first one available. / 1 active-backup Sets an active-backup policy for fault tolerance. Transmissions are received and sent out via the first available bonded member interface. Another bonded member interface is only used if the active bonded member interface fails. / 2 balance-xor Sets an XOR (exclusive-or) policy for fault tolerance and load balancing. Using this method, the interface matches up the incoming request's MAC address with the MAC address for one of the member NICs. Once this link is established, transmissions are sent out sequentially beginning with the first available interface. / 3 broadcast Sets a broadcast policy for fault tolerance. All transmissions are sent on all member interfaces. / 4 802.3ad Sets an IEEE 802.3ad dynamic link aggregation policy. Creates aggregation groups that share the same speed and duplex settings. Transmits and receives on all members in the active aggregator. Requires a switch that is 802.3ad compliant. / 5 balance-tlb Sets a Transmit Load Balancing (TLB) policy for fault tolerance and load balancing. The outgoing traffic is distributed according to the current load on each member interface. Incoming traffic is received by the current member NIC. If the receiving member fails, another member takes over the MAC address of the failed member. / 6 balance-alb Sets an Active Load Balancing (ALB) policy for fault tolerance and load balancing. Includes transmit and receive load balancing for IPV4 traffic. Receive load balancing is achieved through ARP negotiation.
[1]	List of phisical network interfaces int the host: / ifconfig | grep enp | awk '{print $1}' | sed 's/.$//' / Configure Network Bonding.

# display network devices / [root@dlp ~]# nmcli device / DEVICE TYPE STATE CONNECTION / enp1s0 ethernet connected enp1s0 / enp7s0 ethernet disconnected -- / lo loopback unmanaged -- / # delete existing network connections / [root@dlp ~]# nmcli connection delete enp1s0 / Connection 'enp1s0' (0c5a95c5-1c2a-351d-add2-7fee398c96ab) successfully deleted. / [root@dlp ~]# nmcli device / DEVICE TYPE STATE CONNECTION / enp1s0 ethernet disconnected -- / enp7s0 ethernet disconnected -- / lo loopback unmanaged -- / # add a new bonding device [bond0] (any name you like) # refer to the description above for each mode (OK to specify with mode number for [mode=*]) / [root@dlp ~]# nmcli connection add type bond ifname bond0 con-name bond0 bond.options "mode=balance-rr" / Connection 'bond0' (c0c1097e-476e-4c5c-ac5a-3284fb053ce8) successfully added. / # add member devices to the bonding device / [root@dlp ~]# nmcli connection add type ethernet ifname enp1s0 master bond0 / Connection 'bond-slave-enp1s0' (0e799b5a-cc8d-4062-bf0d-927c080863ff) successfully added. [root@dlp ~]# nmcli connection add type ethernet ifname enp7s0 master bond0 / [root@dlp ~]# nmcli connection modify boond0 ipv4.method disabled / Connection 'bond-slave-enp7s0' (d4a65fb1-9a77-40bd-b8be-aa88ce64cc5f) successfully added. / [root@dlp ~]# nmcli device / DEVICE TYPE STATE CONNECTION / bond0 bond connected bond0 / enp1s0 ethernet connected bond-slave-enp1s0 / enp7s0 ethernet connected bond-slave-enp7s0 / lo loopback unmanaged -- / [root@dlp ~]# nmcli connection / NAME UUID TYPE DEVICE / bond0 c0c1097e-476e-4c5c-ac5a-3284fb053ce8 bond bond0 / bond-slave-enp1s0 0e799b5a-cc8d-4062-bf0d-927c080863ff ethernet enp1s0 / bond-slave-enp7s0 d4a65fb1-9a77-40bd-b8be-aa88ce64cc5f ethernet enp7s0 / ================== / # bridge / $ nmcli con add ifname br0 type bridge con-name br0 / $ nmcli con add type bridge-slave ifname bond0 master br0 / $ nmcli connection show / # set IP address and so on to the bridge device and restart it # IP address / [root@dlp ~]# nmcli connection modify br0 ipv4.addresses 10.0.0.30/24 / # gatway / [root@dlp ~]# nmcli connection modify br0 ipv4.gateway 10.0.0.1 / # DNS - specify with space separated if set multiple DNS servers / [root@dlp ~]# nmcli connection modify br0 ipv4.dns "10.0.0.10 10.0.0.11" / # DNS search base - specify with space separated if set multiple domains / [root@dlp ~]# nmcli connection modify br0 ipv4.dns-search "srv.world" / [root@dlp ~]# nmcli connection modify br0 ipv4.method manual / [root@dlp ~]# nmcli connection down br0 && nmcli connection up br0 / nmcli con modify bond0 master br0 slave-type bridge / nmcli con up bond0 / Connection 'bond0' successfully deactivated (D-Bus active path: /org/freedesktop/NetworkManager/ActiveConnection/2) Connection successfully activated (master waiting for slaves) (D-Bus active path: /org/freedesktop/NetworkManager/ActiveConnection/5) / # verify bonding state / [root@dlp ~]# cat /proc/net/bonding/bond0 / Ethernet Channel Bonding Driver: v5.14.0-115.el9.x86_64 / Bonding Mode: load balancing (round-robin) / MII Status: up / MII Polling Interval (ms): 100 / Up Delay (ms): 0 / Down Delay (ms): 0 / Peer Notification Delay (ms): 0 / Slave Interface: enp1s0 / MII Status: up / Speed: Unknown / Duplex: Unknown / Link Failure Count: 0 / Permanent HW addr: 52:54:00:6e:a3:17 / Slave queue ID: 0 / Slave Interface: enp7s0 / MII Status: up / Speed: Unknown / Duplex: Unknown / Link Failure Count: 0 / Permanent HW addr: 52:54:00:fe:cd:82 / Slave queue ID: 0 / [root@dlp ~]# ip address / 1: lo: <LOOPBACK,UP,LOWER_UP> mtu 65536 qdisc noqueue state UNKNOWN group default qlen 1000 / link/loopback 00:00:00:00:00:00 brd 00:00:00:00:00:00 / inet 127.0.0.1/8 scope host lo / valid_lft forever preferred_lft forever / inet6 ::1/128 scope host / valid_lft forever preferred_lft forever / 2: enp1s0: <BROADCAST,MULTICAST,SLAVE,UP,LOWER_UP> mtu 1500 qdisc fq_codel master bond0 state UP group default qlen 1000 / link/ether 52:54:00:6e:a3:17 brd ff:ff:ff:ff:ff:ff / 3: enp7s0: <BROADCAST,MULTICAST,SLAVE,UP,LOWER_UP> mtu 1500 qdisc fq_codel master bond0 state UP group default qlen 1000 / link/ether 52:54:00:6e:a3:17 brd ff:ff:ff:ff:ff:ff permaddr 52:54:00:fe:cd:82 / 5: bond0: <BROADCAST,MULTICAST,MASTER,UP,LOWER_UP> mtu 1500 qdisc noqueue state UP group default qlen 1000 / link/ether 52:54:00:6e:a3:17 brd ff:ff:ff:ff:ff:ff / inet 10.0.0.30/24 brd 10.0.0.255 scope global noprefixroute bond0 / valid_lft forever preferred_lft forever / inet6 fe80::34ce:9e06:c339:558a/64 scope link noprefixroute / valid_lft forever preferred_lft forever / # configuration files are stored under the place / [root@dlp ~]# / ll /etc/NetworkManager/system-connections / total 12 / -rw-------. 1 root root 288 Jun 29 14:27 bond0.nmconnection / -rw-------. 1 root root 153 Jun 29 14:25 bond-slave-enp1s0.nmconnection / -rw-------. 1 root root 153 Jun 29 14:25 bond-slave-enp7s0.nmconnection

Copyright © 2007-2022 Server World All Rights Reserved.