## Chapter 10. Network Configuration
10.1. Network address translation (NAT) with libvirt
10.2. Bridged networking with libvirt
This page provides an introduction to the common networking configurations used by libvirt based applications. This information applies to all hypervisors, whether Xen, KVM or another. For additional information consult the libvirt network architecture docs.
The two common setups are "virtual network" or "shared physical device". The former is identical across all distributions and available out-of-the-box. The latter needs distribution specific manual configuration.
Network services on virtualized guests are not accessible by default from external hosts. You must enable either Network address translation (NAT) ir a network Bridge to allow external hosts access to network services on virtualized guests.
## 10.1. Network address translation (NAT) with libvirt
One of the most common methods for sharing network connections is to use Network address translation (NAT) forwarding (also know as virtual networks).
##### Host configuration
Every standard libvirt installation provides NAT based connectivity to virtual machines out of the box. This is the so called 'default virtual network'. Verify that it is available with the virsh net-list --all command.
# virsh net-list --all
Name State Autostart
-----------------------------------------
default active yes
If it is missing, the example XML configuration file can be reloaded and activated:
# virsh net-define /usr/share/libvirt/networks/default.xml
The default network is defined from /usr/share/libvirt/networks/default.xml
Mark the default network to automatically start:
# virsh net-autostart default
Network default marked as autostarted
Start the default network:
# virsh net-start default
Network default started
Once the libvirt default network is running, you will see an isolated bridge device. This device does not have any physical interfaces added, since it uses NAT and IP forwarding to connect to outside world. Do not add new interfaces.
# brctl show
bridge name bridge id STP enabled interfaces
virbr0 8000.000000000000 yes
libvirt adds iptables rules which allow traffic to and from guests attached to the virbr0 device in the INPUT, FORWARD, OUTPUT and POSTROUTING chains. libvirt then attempts to enable the ip_forward parameter. Some other applications may disable ip_forward, so the best option is to add the following to /etc/sysctl.conf.
 net.ipv4.ip_forward = 1
##### Guest configuration
Once the host configuration is complete, a guest can be connected to the virtual network based on its name. To connect a guest to the 'default' virtual network, the following XML can be used in the guest:
<interface type='network'>
  <source network='default'/>
</interface>
## Note
Defining a MAC address is optional. A MAC address is automatically generated if omitted. Manually setting the MAC address is useful in certain situations.
<interface type='network'>
  <source network='default'/>
  <mac address='00:16:3e:1a:b3:4a'/>
  </interface>
## 10.2. Bridged networking with libvirt
Bridged networking (also known as physical device sharing) is used for dedicating a physical device to a virtual machine. Bridging is often used for more advanced setups and on servers with multiple network interfaces.
##### Disable Xen network scripts
If your system was using a Xen bridge, it is recommended to disable the default Xen network bridge by editing /etc/xen/xend-config.sxp and changing the line:
 (network-script network-bridge)
To:
 (network-script /bin/true)
##### Disable NetworkManager
NetworkManager does not support bridging. Running NetworkManager will overwrite any manual bridge configuration. Because of this, NetworkManager should be disabled in order to use networking via the network scripts (located in the /etc/sysconfig/network-scripts/ directory):
# chkconfig NetworkManager off
# chkconfig network on
# service NetworkManager stop
# service network start
## Note
As an alternative to turning off NetworkManager, add "NM_CONTROLLED=no" to the ifcfg-* scripts used in the examples. If you do not either set this parameter or disable NetworkManager entirely, any bridge configuration will be overwritten and lost when NetworkManager next starts.
##### Creating network initscripts
Create or edit the following two network configuration files. This step can be repeated (with different names) for additional network bridges.
Change to the /etc/sysconfig/network-scripts directory:
# cd /etc/sysconfig/network-scripts
Open the network script for the device you are adding to the bridge. In this example, ifcfg-eth0 defines the physical network interface which is set as part of a bridge:
DEVICE=eth0
# change the hardware address to match the hardware address your NIC uses
HWADDR=00:16:76:D6:C9:45
ONBOOT=yes
BRIDGE=br0
## Tip
You can configure the device's Maximum Transfer Unit (MTU) by appending an MTU variable to the end of the configuration file.
MTU=9000
Create a new network script in the /etc/sysconfig/network-scripts directory called ifcfg-br0 or similar. The br0 is the name of the bridge, this can be anything as long as the name of the file is the same as the DEVICE parameter.
DEVICE=br0
TYPE=Bridge
BOOTPROTO=dhcp
ONBOOT=yes
DELAY=0
## Warning
The line, TYPE=Bridge, is case-sensitive. It must have uppercase 'B' and lower case 'ridge'.
After configuring, restart networking or reboot.
# service network restart
Configure iptables to allow all traffic to be forwarded across the bridge.
# iptables -I FORWARD -m physdev --physdev-is-bridged -j ACCEPT
# service iptables save
# service iptables restart
## Disable iptables on bridges
Alternatively, prevent bridged traffic from being processed by iptables rules. In /etc/sysctl.conf append the following lines:
net.bridge.bridge-nf-call-ip6tables = 0
net.bridge.bridge-nf-call-iptables = 0
net.bridge.bridge-nf-call-arptables = 0
Reload the kernel parameters configured with sysctl.
# sysctl -p /etc/sysctl.conf
Restart the libvirt daemon.
# service libvirtd reload
You should now have a "shared physical device", which guests can be attached and have full LAN access. Verify your new bridge:
# brctl show
bridge name bridge id STP enabled interfaces
virbr0 8000.000000000000 yes
br0 8000.000e0cb30550 no eth0
Note, the bridge is completely independent of the virbr0 bridge. Do not attempt to attach a physical device to virbr0. The virbr0 bridge is only for Network Address Translation (NAT) connectivity.
## Chapter 11. Pre-Red Hat Enterprise Linux 5.4 Xen networking
11.1. Configuring multiple guest network bridges to use multiple Ethernet cards
11.2. Red Hat Enterprise Linux 5.0 laptop network configuration
This chapter covers special topics for networking and network configuration with the Xen hypervisor.
Most guest network configuration occurs during the guest initialization and installation process. To learn about configuring networking during the guest installation process, read the relevant sections of the installation process, Chapter 7, Virtualized guest installation overview.
Network configuration is also covered in the tool specific reference chapters for virsh (Chapter 25, Managing guests with virsh) and virt-manager (Chapter 26, Managing guests with the Virtual Machine Manager (virt-manager)). Those chapters provide a detailed description of the networking configuration tasks using both tools.
## Tip
Using para-virtualized network drivers improves performance on fully virtualized Linux guests. Chapter 12, Xen Para-virtualized Drivers explains how to utilize para-virtualized network drivers.
## 11.1. Configuring multiple guest network bridges to use multiple Ethernet cards
Process to setup network bridges (with the Xen hypervisor):
1. Configure another network interface using either the system-config-network application. Alternatively, create a new configuration file named ifcfg-ethX in the /etc/sysconfig/network-scripts/ directory where X is any number not already in use. Below is an example configuration file for a second network interface called eth1
  $ cat /etc/sysconfig/network-scripts/ifcfg-eth1
  DEVICE=eth1
  BOOTPROTO=static
  ONBOOT=yes
  USERCTL=no
  IPV6INIT=no
  PEERDNS=yes
  TYPE=Ethernet
  NETMASK=255.255.255.0
  IPADDR=10.1.1.1
  GATEWAY=10.1.1.254
  ARP=yes
2. Copy the file, /etc/xen/scripts/network-bridge, to /etc/xen/scripts/network-bridge.xen.
3. Comment out any existing network scripts in /etc/xen/xend-config.sxp and add the line (network-xen-multi-bridge). A typical xend-config.sxp file should have the following line. Comment this line out. Use the # symbol to comment out lines.
  network-script network-bridge
  Below is the commented out line and the new line, containing the network-xen-multi-bridge parameter to enable multiple network bridges.
  #network-script network-bridge
  network-script network-xen-multi-bridge
4. Create a script to create multiple network bridges. This example creates a script called network-xen-multi-bridge.sh in the /etc/xen/scripts/ directory. A sample scripts is below, this example script will create two Xen network bridges (xenbr0 and xenbr1) one will be attached to eth1 and the other one to eth0. If you want to create additional bridges just follow the example in the script and copy nad paste the lines as required:
  #!/bin/sh
  # network-xen-multi-bridge
  # Exit if anything goes wrong.
  set -e
  # First arg is the operation.
  OP=$1
  shift
  script=/etc/xen/scripts/network-bridge.xen
  case ${OP} in
  start)
  $script start vifnum=1 bridge=xenbr1 netdev=eth1
  $script start vifnum=0 bridge=xenbr0 netdev=eth0
  ;;
  stop)
  $script stop vifnum=1 bridge=xenbr1 netdev=eth1
  $script stop vifnum=0 bridge=xenbr0 netdev=eth0
  ;;
  status)
  $script status vifnum=1 bridge=xenbr1 netdev=eth1
  $script status vifnum=0 bridge=xenbr0 netdev=eth0
  ;;
  *)
  echo 'Unknown command: ' ${OP}
  echo 'Valid commands are: start, stop, status'
  exit 1
  esac
5. Make the script executable.
  # chmod +x /etc/xen/scripts/network-xen-multi-bridge.sh
6. Restart networking or restart the system to activate the bridges.
  # service network restart
Multiple bridges should now be configured for guests on the Xen hypervisor.